# S E M I N A R

## Room 119D ZEC

Monday, March 1, 2004, 3:00 p.m. 3:50 p.m.

###### DESIGN OF FREQUENCY SYNTHESIZERS FOR

###### SHORT RANGE WIRELESS TRANSCEIVERS

by

Ari Yakov Vcalero López

#### Texas A&M University

College Station, Texas

Abstract: The rapid growth of the market for short-range wireless devices, with standards such as Bluetooth and Wireless LAN (IEEE 802.11) being the most important, has created a need for highly integrated transceivers that target drastic power and area reduction while providing a high level of integration. The radio section of the devices designed to establish communications using these standards is the limiting factor of the power reduction efforts. A key building block in a transceiver is the frequency synthesizer, since it operates at the highest frequency of the system and consumes a very large portion of the total power in the radio.

A frequency synthesizer integrated within a dual-mode receiver capable of processing signals of the Bluetooth and Wireless LAN (IEEE 802.11b) standards will be presented. The frequency synthesizer, implemented in BiCMOS technology, operates the voltage controlled oscillator at twice the required frequency to generate quadrature signals by dividing-by-two the VCO output. A phase switching prescaler is featured in the synthesizer. This prescaler ensures a robust operation by inverting the switching order in traditional architectures. A large capacitance is integrated on-chip using a capacitance multiplier circuit that provides a drastic area reduction (more than 60%) while adding a negligible noise contribution to the phase noise of the synthesizer.

As an addition to the frequency synthesizer, a self-calibrated quadrature generator is included. The operation range of the VCO is extended to cover a frequency band from 4.8GHz to 5.85GHz. By doing this, the synthesizer is capable of generating LO signals for Bluetooth and IEEE 802.11a, b and g standards. The quadrature output of the 5 – 6 GHz signal is generated through a first order RC – CR network with an automatic calibration loop. The loop uses a high frequency phase detector to measure the deviation from the 90( separation between the I and Q branches and implements an iterative algorithm to minimize the phase errors between the I and Q branches and their differential counterparts.

Ari Yakov Valero López was born in Mexico City, Mexico in 1972. He received the B.S in Communications and Electronics Engineering degree from University of Guanajuato, Guanajuato, Mexico in 1996, and the M.S.E.E. degree from the National Institute for Astrophysics, Optics and Electronics (INAOE), Puebla, Mexico, in 1998 where he worked in the design of clock and data recovery circuits. During the Fall of 1997 he was a Visiting Scholar in the Analog and Mixed Signal Center in Texas A&M University. Since 1999 he has been working towards the Ph.D. degree at the Analog and Mixed Signal Center, Texas A&M University, College Station, TX. During his Ph.D. program he has been involved in the design of two receivers for short-range wireless communications. He is a co-recipient of the third best student paper award in RFIC, Seattle 2002. His current field of research is in the design and fabrication of analog and mixed-signal circuits and frequency synthesizers for communication systems.