# S E M I N A R

## Room 223A ZEC

Tuesday, August 30, 2005, 3:55 p.m. -  5:10 p.m.

by

#### Artur Lewinski

Texas A&M University

Analog Mixed-Signal

#### College Station, Texas

High Frequency and High Dynamic Range Continuous Time Filters

Abstract: Many modern communication systems use Orthogonal Frequency Division Multiplexing (OFDM) and Discrete Multi-tone (DMT) as modulation schemes where high data rates are transmitted over a wide frequency band in multiple orthogonal sub-carriers. Due to its many advantages such as flexibility, good noise immunity and the ability to be optimized for medium conditions its use can be found in Digital video broadcasting, local area wireless network (IEEE 802.11a), Asymmetric Digital Subscriber Line (ADSL), Very High Bit Rate DSL (VDSL) and power line communications (PLC). However, a major challenge is the design of the analog front-end; for these systems a large dynamic range is required due to the significant peak to average ratio of the resulting signals. In receivers, very demanding high-performance analog filters are typically used to block interferers and provide anti-aliasing before the subsequent analog to digital conversion stage.

For frequencies higher than 10MHz, Gm-C filter implementations are generally preferred due to the more efficient operation of wide-band operational transconductance amplifiers (OTA). Nevertheless, the inherent low-linearity of open-loop operated OTA limits the dynamic range.  In this seminar, three different proposed OTA linearity enhancement techniques for the design of high frequency and high dynamic range will be presented. Simulation and experimental results of a 30MHz fifth order low-pass elliptic filter implementation show a Spurious Free Dynamic Range (SFDR) of 65dB with a power consumption of 85mW. In a figure of merit where SFDR is normalized to the power consumption, this filter is 6dB above the trend-line of recently reported continuous time filters.

Artur Lewinski obtained his bachelor degree with honors in Electronics Engineering in 2000 in the Instituto Tecnologico de Queretaro in Queretaro, Mexico. Currently he is Ph.D. Student in the Analog & Mixed Signal Center in the Electrical Engineering faculty of the Texas A&M University. His research work focuses on the dynamic range enhancement of high frequency continuous time filters. During the fall of 2001 he was interning in the Data Acquisition group at Cirrus Logic. His interest areas are in analog signal processing, programmable continuous-time filters and mixed-signal interface circuits.