# SEMINAR

## Room 223A ZEC

Tuesday, November 22, 2005, 3:55 p.m. – 5:10 p.m.

DESIGN OF RF/IF ANALOG TO DIGITIAL CONVERTERS FOR

SOFTWARE RADIO COMMUNICATION RECEIVERS

by

### Bharath Kumar Thandri

Graduate Student

Analog and Mixed Signal

### Texas A&M University

Abstract : The growing need for support of multiple wireless standards in the same chip has led to search for better transceiver architectures than the traditional superheterodyne architecture. Software radio transceiver architecture has been proposed to simplify multiple wireless standards support by defining the modulation and demodulation waveforms in software running in a DSP, which requires the A/D and D/A conversion to occur as close to the antenna as possible in a transceiver chain. This talk will focus on the design of radio frequency (RF) and intermediate frequency (IF) ADC’s for software radio receiver architectures. The first part of the presentation will feature a short tutorial on design approaches and major non-idealities of continuous time sigma-delta ADC’s. Two designs that have been completed in this research will then be presented. The first design is a 75 mW, 3.8 Gs/s, 11 bit RF ADC implemented in IBM 0.25 (m SiGe BiCMOS technology. Measurement results show SNR of 68 dB and 61 dB in bandwidths of 200 kHz and 1 MHz around 950 MHz center frequency. The second design is a 125 MHz IF ADC implemented in TSMC 0.35 (m CMOS technology with a clock frequency of 500 MHz, and uses a digital tuning scheme to obtain best SNR performance.

Bharath Kumar Thandri received B.E. (Hons) in Computer Science from BITS, Pilani, India in May 1998 and M.S. in Electrical engineering from AMSC, Texas A&M University in Dec 2001. He has been working towards his PhD since Jan 2003 in AMSC group on the design of ADC’s for software radio communication receivers. He worked as design engineer in Cypress semiconductors, Austin, Texas in 2002 on mixed signal CAD flow development and design of optical communication transceiver IC’s. From June 1998 to Aug 199, he worked in theDSP group of Texas Instruments (India) Ltd, Bangalore on the development of software simulators for TI C6x DSP’s. His main research interests are in the area of high performance and high frequency analog and mixed signal circuits for communication and signal processing IC’s.