# S E M I N A R

## Room 227A ZEC

Thursday, September 27, 2007    3:55 - 5:10 P.M.

Design Methodologies for Built-In Testing of Integrated RF

Transceivers with the On-Chip Loopback Technique

by

Marvin Onabajo

Texas A&M University

Analog and Mixed-Signal Center

Abstract:   Advances towards increased integration and complexity of radio frequency (RF) and mixed-signal integrated circuits reduce the effectiveness of contemporary test methodologies and result in a rising cost of testing. The focus in the research that will be addressed is on the circuit-level realizations of alternative test strategies for integrated wireless transceivers with the goal to lower the test cost.

The implementation of an on-chip loopback block will be discussed to close the signal path between the transmitter and receiver sections of integrated transceivers in self-test mode for characterization of RF front-end blocks with on-chip power detectors and bit error rate analysis at low frequencies. The loopback circuit is intended for transceivers operating in the 1.9-2.4GHz range and was designed to compensate for transmitter-receiver offset frequency differences from 40MHz to 200MHz, having 11-27dB continuous attenuation control and consuming 0.052mm2 die area in 0.13μm CMOS technology.

Another circuit that will be presented is a current generator for built-in testing of impedance-matched RF front-end blocks with current injection. Since this circuit has relatively high output impedance (>1kΩ up to 2.4GHz), it does not influence the input matching network of the low-noise amplifier (LNA) under test. The current generator was employed together with two power detectors in a current injection built-in test for a LNA with 14% total layout area overhead in 0.13μm CMOS technology. The post-layout simulation results showed that the LNA gain (S21) estimation with the external matching network was within 3% of the actual gain.

Marvin Onabajo received his B.S. in Electrical Engineering from The University of Texas at Arlington in December 2003, where he worked in the Analog and Mixed-Signal IC group during his final year in affiliation with the National Science Foundation’s Research Experiences for Undergraduates program. From 2004 to 2005, he was Electrical Test Process/Product Engineer at Intel Corp. in Hillsboro, Oregon. He has been a member of the Analog and Mixed-Signal Center at Texas A&M University since August 2005 and is currently engaged in research involving analog built-in testing.