# S E M I N A R

## Room 223D ZEC

Thursday, November 20, 2008    3:55 - 5:10 P.M.

###### A High PSR Low Drop-out Regulator using Feed-Forward Ripple Cancellation Technique

by

Ahmed Amer

Texas A&M University

Analog Mixed-Signal Center

Abstract: Low drop-out (LDO) linear regulators have become a key building block in portable communication systems for power management ICs. The LDO usually comes after a switching DC-DC converter to reduce the output ripples providing a regulated voltage source for noise-sensitive blocks. For a higher level of integration, there is a need to increase the operating frequency of the switching converters. This necessitates a following LDO regulator with high ripple rejection at frequencies up to several megahertz.   A feed-forward ripple cancellation technique is applied to an LDO regulator to achieve a high power supply rejection (PSR) along a wide frequency range. The LDO is implemented in 0.13µm CMOS technology and supplies current up to 25mA with a minimum drop-out voltage of 0.15V. The measured PSR shows a rejection better than -56dB up to 10MHz, while consuming a quiescent current of 50µA with the bandgap included.

Ahmed Amer received the B.Sc. degree in electronics and communications (magna sum laude), and the M.Sc. degree in electronic engineering, both from Ain Shams University, Cairo, Egypt, in 2002 and 2006, respectively. Since 2007, he has been pursuing the Ph.D. degree from Texas A&M University in the area of Analog and RF circuit design. From 2002 to 2006, He was a teaching and research assistant in the Electronics and Communications Engineering Department at Ain Shams University. From 2004 to 2006 he has been working as an RFIC Design Engineer in SysDSoft Inc., Cairo, Egypt. From May to August 2008 he was an intern with Texas Instruments, Dallas, TX. His research interests include power management electronics, biomedical electronics and RF IC design.