# S E M I N A R

## Room 223D ZEC

Monday, September 19, 2011    3:00-3:50 P.M.

Design and Implementation of a CMOS Baseband Transimpedance

Amplifier Robust Against Out-of-Band Blockers

by

Alfredo Pérez-Carrillo

Texas A&M University

AMSC

Abstract Transimpedance amplifiers are commonly used in zero-IF receivers as the terminating load for passive mixers. In addition to converting current signals into a voltage, their low input impedance is beneficial for minimizing distortion due to the non-linear resistance of the switches. For systems in which multiple radios coexist and, consequently, interferers abound due to the collocation or proximity of neighbor radios, the out of band (OOB) linearity of the TIA can be highly significant to receiver performance. When strong interferers are downconverted to frequencies near the edge of the desired channel bandwidth, distortion in the TIA can induce blocking, cross modulation, and/or intermodulation products in band degrading receiver sensitivity. Addressing the subject, a TIA robust against blocking signals OOB is presented. Active feedback and class AB biasing are exploited in its topology to achieve a high -1dB compression point in band under the presence of blockers across a wide range of frequencies (0.05-1 GHz). A prototype of the proposed solution has been fabricated in a 45nm CMOS process and experimental results verify that, for a 10 MHz channel bandwidth, the proposed design reaches OOB and in band -1dB compression at signal levels of ±10 mA and ±9 mA, respectively, with blockers present at 50 MHz and beyond.

Alfredo Pérez-Carrillo received the B.S. (cum laude) and M.S. degrees in Electrical Engineering from The University of Texas at El Paso in 2002 and 2005, respectively. He is currently pursuing the Ph.D. degree at Texas A&M University. From 2008 to 2010 he was a fellow for the National Science Foundation’s Graduate STEM Fellows in K-12 Education Program. As a graduate technical intern at Intel Corporation in the summer of 2009, he designed analog baseband circuits for wireless communication receivers. His current research interests include highly-linear analog baseband design and broadband RF front-ends.