# S E M I N A R

## Room 223D ZEC

Monday, October 31, 2011    3:00-3:50 P.M.

by

Atul A. Aranke

Texas Instruments, Inc.

Dallas, Texas

Qualification of Semiconductor Devices and Challenges

Abstract: For a semiconductor product to be successful in its end application over its life time, the product needs to meet qualification requirements. Requirements include device reliability, actual silicon adhering to the customer/design specification and must be capable of being manufactured in mass production with low defective parts per million (DPPM). The first part of the talk provides an overview of various device reliability requirements incl. electrostatic discharge (ESD), Latch-up (LU), High Temperature Operating Life (HTOL) and also provides insights into device characterization, yield enhancement activities undertaken by Product Development Engineers during device development phase.

Charge Discharge Model (CDM) is one of the device reliability specifications that a semiconductor product should meet. CDM performance depends on the surface area of the silicon/package size. While designing an ESD cell for an I/O pin, first consideration is to estimate the electrical peak discharge current that would be seen under the CDM specification. This current level can be determined from the package(s) that will be used for this IC In the second part of the talk, a case study demonstrating the behavior of electrical peak discharge current with applied voltage for 2 different packages will be presented. The two packages are Think Quad Flat Pack (TQFP) and a custom Printed Circuit Card assembly (PCCA).

Atul A. Aranke obtained Bachelors in Electrical Engineering from University of Nagpur, India (1995) and Masters of Science in Electrical Engineering from University of Texas at Arlington (2002). Prior to joining Texas Instruments Inc., Atul worked as a Business Development Engineer for Oil/Gas and Refinery projects for Siemens in India.

During his time in Texas Instruments Inc., he has worked as a Product Sustaining Engineer and more recently as a New Product Development Engineering Manager. Currently he is the Product and Test Engineering Manager in Storage Product/High Volume Analog. His responsibilities include timely qualification and release to market of preamplifiers used in hard disk drives (HDD).