# S E M I N A R

## Room 223B ZEC

Thursday, October 28, 2010    3:55 - 5:10 P.M.

Integrated AC Current Sensor

by

Axel Thomsen

Distinguished Engineer

Silicon Laboratories Inc.

Austin, TX

Abstract: A difficult task in Switching Mode Power Supplies of higher power levels is the sensing of currents. All typical solutions have significant drawbacks: current transformers are rather bulky and expensive. Shunts are lossy or produce very small signals. DCR circuits lack accuracy as they try to match the parasitics in the coil. The Rogowski coil is a 100 year old current measurement technique. A coil captures the flux change associated with a current change. After integration, the current can be determined. Usually this arrangement is just as bulky as a current transformer, but IC technology together with innovative packaging allows the integration of the Rogowski coil with the signal conditioning electronics into a 5x5mm IC in a plastic package. The resolution achieved is 10% over PVT after a single point factory calibration.

Axel Thomsen was born in Hamburg, Germany in 1965. He attended the Polytechnical University of Braunschweig, Germany, from 1984 to 1988. From 1988 to 1992 he attended Georgia Institute of Technology, where he received his Ph. D. in Electrical Engineering in the area of analog IC design. From 1993 to 1995 he was Assistant Professor at the University of Alabama in Huntsville. From 1995 to 2001 he was a design engineer and manager at Cirrus Logic in Austin where he worked on multistage amplifiers and high resolution data converters.

He is currently a distinguished engineer at Silicon Laboratories, where he has worked on low jitter timing circuits, PLLs, and ICs for power and isolation applications. Occasionally he teaches analog IC design at UT Austin. He holds 35 patents and has published 20 papers.