# S E M I N A R

## Room 223C ZEC

Thursday, October 22, 2009    3:55 - 5:10 P.M.

Calibrated Continuous-Time Bandpass Delta-Sigma Modulator for Next Generation Wireless Device

by

Cho-Ying Lu

Graduate Student

Analog Mixed-Signal

Abstract: Based on the tremendous development on semiconductor and wireless communication, the concept of next generation receiver to integrate different wireless services into a single chip-set is popular. Comparing with other receiver architectures, the high-IF architecture has potential to be competitive in this application because of its inherent advantages, such as no DC offset insensitivity to flicker noise and relaxed image effect. However, the ADC in this architecture is a bottleneck. Therefore, this talk will discuss the requirements of the ADC and also show the design of a continuous-time bandpass delta-sigma modulator, which can fulfill all the specifications of the ADC in next generation receiver with high-IF architecture. In addition, a unique software-based calibration scheme that corrects the performance of the modulator robustly without any extra power-hungry analog circuitry is discussed.

Cho-Ying Lu is currently pursuing his Ph.D. degree at the group of Analog and Mixed-Signal Center, department of Electrical and Computer Engineering, Texas A&M University, College Station, Texas. He received B.S. degree in Electrical Engineering and M.S. degree in Electronic Engineering from National Tsing Hua University, Hsinchu, Taiwan at 2002 and 2004 respectively. From Aug. 2007 to Dec. 2007, he was with the Wireless group, Texas Instruments, Inc., Dallas, Texas, as a co-op, working on receiver system planning of HD radio and DAB (Digital Audio Broadcasting).  His research interests are mainly in the design of wide-bandwidth high-resolution continuous-time Delta-Sigma ADC.