# S E M I N A R

## Room 223D ZEC

Monday, September 5, 2011    3:00 - 3:50 P.M.

A 2 GHz Highly Linear Dual Mode BiCMOS Power Amplifier Using a Reconfigurable Matching Network

by

Hajir Hedayati

Texas A&M University

AMSC

Abstract: A highly linear, efficient two stage power amplifier for high data rate wireless applications is presented. The linearity is greatly improved by adding an auxiliary amplifier to the main bipolar junction transistor (BJT) in a feed-forward approach to cancel out the non-linearity terms. The output power is increased by a second harmonic current degradation which improves the PA linearity as well. The efficiency enhancement is achieved using a switchable biasing and a reconfigurable output matching network based on the available input power which is monitored by an on chip envelope detector. The PA is fabricated in 0.25 µm BiCMOS technology. The PA works at 2 GHz with supply voltages of 2.5 V and 1.7 V. The experimental results show a gain of 13 dB and a maximum output power of 23 dBm with a PAE of 38%. The 1 dB output power compression point is 21 dBm with a 32% PAE. The 6 dB power back-off PAE is 23%. The IM3 and IM5 terms are 41 dB and 44 dB below the fundamental tone for the 21 dBm average output power.

Hajir Hedayati was born in Oroumieh, Iran in 1985. He received his Master’s  degree in electrical engineering from Sharif University of Technology, Tehran, Iran, in 2009. He joined TAMU at Spring 2010. He is currently working toward the Ph. D. degree in the Analog and Mixed Signal Center (AMSC), Texas A&M University, College Station, Texas. His research interests include the analysis and development of integrated circuits for low power in-band interference tolerant Ultra-Wideband Transceivers and low power narrow band Transceivers.