# S E M I N A R

## Room 223C ZEC

Thursday, November 19, 2009    3:55 - 5:10 P.M.

Aperture and Noise Analysis of Clocked Comparators

by

Dr. Jaeha Kim

Stanford University

Abstract: This talk describes ways to analyze and simulate two key characteristics of clocked comparators: aperture and noise. While comparators are inherently nonlinear, turning analog signals into binary decisions, these characteristics can be related to a linear, time-varying model (LTV) of the circuit. For example, the sampling aperture of a comparator is equivalent to an impulse sensitivity function (ISF) of oscillators, the term first coined by Hajimiri and Lee in 1998. The similar LTV noise analysis can explain the random decision errors in these comparators, gaining more significance in low-voltage high-resolution ADCs and data receivers. The talk will also address ways to simulate these characteristics using the periodic analysis available from RF circuit simulators.

Jaeha Kim is currently an Acting Assistant Professor at Stanford University and his research interests include low-power mixed-signal systems and their design methodologies. He received the B.S. degree in electrical engineering from Seoul National University, Korea in 1997 and received the M.S. and Ph.D. degrees in electrical engineering from Stanford in 1999 and 2003, respectively. Previously, he was with True Circuits as Circuit Designer, with Seoul National University as Post-doctoral Researcher, and most recently with Rambus, Inc. as Principal Engineer. Dr. Kim is a recipient of the Takuo Sugano award for outstanding far-east paper at 2005 International Solid-State Circuits Conference (ISSCC) and the Low Power Design Contest Award at 2001 International Symposium on Low Power Electronics and Design (ISLPED).