# S E M I N A R

## Room 223D ZEC

Thursday, September 4,  2008    3:55 - 5:10 P.M.

Title: A Highly Linear, 1.3GHz, 24mW Dual-Path Current Mode Filter

by

Manisha Gambhir

Texas A&M Univeristy

College Station, Texas

Abstract: Wideband Continuous time filters for data communication applications rely on ‘open-loop’ transconductors. The linearity performance of such transconductors directly limits the power efficiency of the whole filter. This had spurred a significant body of research in OTA linearization over the past two decades. A simple, wideband structure, ‘Nauta’s Transconductor’, is known to be quite linear and power efficient due to its complementary class A-B action. However, practical applicability of this structure is limited due to its susceptibility to supply noise and sensitivity of the bias point to VT and process variations.

In this seminar, a class-AB, dual path building block for Gm-C filters is presented. The class-AB action provides good linearity and Gm/Id efficiency while the proposed dual path approach solves the PSRR problem associated with a conventional Nauta’s transconductor. A current-mode 4th order Butterworth filter is designed using the proposed building block in 0.13m UMC technology and the experimental results are presented. The seminar is concluded with a discussion on the proposed current mode block and its salient features.

Manisha Gambhir received the B.E. degree in Electronics and Communication Engineering from Delhi University, New Delhi, India in 2001 and M.S. degree in Electrical Engineering from Texas A&M University, College Station, TX.

She is currently working towards her Ph.D. at Texas A&M University College Station, TX. From 2001-2003 she was with Texas Instruments, Bangalore, India where she was involved in the design of analog to digital converters for ADSL applications. During the summer of 2004, she interned at the wireless division in Silicon Laboratories, Austin, TX. In the fall of 2005, she was a design intern with the Read-Channel group at Agere Systems, Allentown, PA where she deigned low power GHz-range ADCs for read-channel applications. Her current research interests include high speed mixed-signal analog design, filters and data converters.