# S E M I N A R

## Room 104A ZEC

Thursday, January 28, 2010    3:55 - 5:10 P.M.

Design of Linear OTA-C Filters over Wide Frequency Ranges

by

Mohamed Mobarak

Texas A&M University

College Station, TX

Abstract: An architectural attenuation-predistortion linearization scheme for a wide range of operational transconductance amplifiers (OTAs) is proposed and demonstrated with a transconductance-capacitor (Gm-C) filter. The linearization technique utilizes two matched OTAs to cancel output harmonics, creating a robust architecture. Compensation for process variations and frequency-dependent distortion based on Volterra series analysis is achieved by employing a delay equalization scheme with on-chip programmable resistors.

An OTA design with the proposed broadband linearization method has third-order inter-modulation (IM3) distortion better than -74dB up to 350MHz with 0.2Vpp input, 70dB signal-to-noise ratio (SNR) in 1MHz bandwidth, and 5.2mW power consumption. The distortion-cancellation technique enables an IM3 improvement of up to 22dB compared to a commensurate OTA without linearization. A proof-of-concept lowpass filter with the linearized OTAs has a measured IM3 < -70dB and 54.5dB dynamic range over its 195MHz bandwidth. The standalone OTAs and the filter were fabricated on a 0.13μm CMOS test chip with 1.2V supply.

Mohamed Mobarak was born in Cairo, Egypt, in 1979. He received his B.Sc. (with honors) and M.Sc. in electronics and communications engineering from Cairo University, Egypt in 2001 and 2004, respectively. He is currently working towards his Ph.D. in the Analog and Mixed-Signal Center, Texas A&M University, College Station, TX. From May 2006 to January 2007, he was an intern at Hittite Microwave, where he worked on frequency synthesizers. From May 2009 to September 2009, he interned at Microtune Inc., where he designed a cable modem upstream Amplifier for the DOCSIS 3.0 standard. His current research interests include high-efficiency power amplifiers, highly linear filters, and frequency synthesizers.