# S E M I N A R

## Room 223C ZEC

Thursday, February 10, 2011    3:55 - 5:10 P.M.

Optimization of Switched Capacitor DC-DC converter

by

Kyoohyun Noh

Texas A&M University

AMSC

Abstract: As the necessity for multiple power supply voltage levels has become critical for modern integrated circuits, switched capacitor DC-DC converters have emerged as a promising potential solution to efficient power delivery in low power or medium power applications. This talk presents a switched capacitor DC-DC converter optimization methodology that predicts the optimal efficiency for a particular switched capacitor DC-DC converter topology as a function of power density. In the low power density region, the efficiency is limited by bottom plate capacitance, whereas the balance between switch driving loss and slow switching loss is the limiting factor in the high power density region. Moreover, we can change the switching frequency of the converter to linearly regulate down the output voltage, which makes it possible to generate an arbitrary conversion gain with high efficiency.

Kyoohyun Noh (S’08) received the B.S. degree in electrical engineering from Seoul National University, Seoul, Korea, in 2004, and the M.S. degree from the University of California at Berkeley in 2010, and is currently working toward the Ph.D. degree at Texas A&M University under the guidance of Prof. Edgar Snchez-Sinencio.

He had internships in Samsung electronics and Hynix semiconductor. From 2006 to 2007, he was a research intern with ISDL, Seoul National University, where he worked on pipelined ADC architecture for gigabit Ethernet. His current research interests include energy efficient high performance ADC and analog-mixed signal integrated circuits and systems for medical and power applications.