# S E M I N A R

## Room 104A ZEC

Thursday, February 25, 2010    3:55 - 5:10 P.M.

Hybrid Feedback DAC Clock-Jitter Error Shaping Technique for Continuous-Time

ΔADCs

by

Ramy Ahmed

Texas A&M University

College Station, TX

Abstract: Continuous-time (CT) Δ analog-to-digital converters (ADCs) have gained significant attention in wideband receivers, because of their amenability for operating at a higher-speed with lower power consumption compared to discrete-time counterparts, inherent anti-aliasing, and robustness to sampling errors in the quantizer. Although robust, CT Δmodulators suffer from a critical limitation due to their high sensitivity to the clock-jitter in the feedback digital-to-analog converter (DAC) sampling clock.

A simple hybrid error spectral shaping solution for the feedback DAC pulse-width jitter problem in CT Δ ADCs is presented. The proposed technique features an effecient combination between the conventional rectangular-pulse switched-current (SI) DAC and a discrete-time switched-capacitor (SC) DAC to achieve efficient spectral shaping for the jitter induced error in the modulator’s feedback signal. Simulation results show that the jitter tolerance of the proposed hybrid error shaping solution is equivalent to that of the commonly used jitter-tolerant exponentially-decaying waveform switched-capacitor-resistor (SCR) DAC structure, but  at much more relaxed slew-rate (SR) requirement on the op-amp used in the modulator’s loop filter, which translates into significant power savings.

Ramy Ahmed was born in Cairo, Egypt in 1981. He received his B.Sc. and M.Sc. in electronics and communications engineering from Cairo University, Egypt in 2004 and 2007, respectively. He is currently working towards his Ph.D. in the Analog and Mixed-Signal Center (AMSC), Texas A&M University, College Station, TX. During spring 2008, he was an intern at Rice Automated Nanoscale Design Group (RAND), Rice University, Houston, TX, where he was working on non-autonomous chaotic oscillators and 60 GHz receivers. His research interests include data converters and multi-standard wireless receivers.