# S E M I N A R

## Room 223D ZEC

Monday, November 21, 2011    3:00-3:50 P.M.

Jitter Tolerance in Continuous-Time Δ ADCs: A Hybrid Feedback DAC Based on Spectral Shaping of Jitter Induced Errors

by

Ramy Ahmed

Texas A&M University

College Station, TX

Abstract: Continuous-time (CT) Δ analog-to-digital converters (ADCs) have gained significant attention in wideband receivers, because of their amenability to operate at a higher-speed with lower power consumption compared to discrete-time counterparts, inherent anti-aliasing, and robustness to sampling errors in the quantizer. However, CT Δ modulators suffer from a critical limitation due to their high sensitivity to the clock-jitter in the feedback digital-to-analog converter (DAC) sampling clock. A simple hybrid DAC solution is presented that achieves tolerance to DAC pulse-width jitter errors by spectrally shaping the jitter induced errors in the feedback DAC. The proposed technique features an effecient combination between the conventional rectangular-pulse switched-current (SI) DAC and a discrete-time switched-capacitor (SC) DAC to achieve spectral shaping for the jitter induced error in the modulator’s feedback signal. As a prove of concept, a 384 MHz second-order single-bit CT Δ modulator for WCDMA baseband channel of 1.92 MHz has been designed using the proposed feedback hybrid DAC structure. The Δmodulator is designed in a 1.2 V, 90nm, IBM 9LP CMOS process. A maximum signal-to-noise-plus-distortion ratio (SNDR) of 68 dB over a 1.92 MHz bandwidth is achieved, while consuming 3.44 mW. Simulation results show 20 dB robustness to PWJ over the commonly used non-return-to-zero DACs.

Ramy Ahmed was born in Cairo, Egypt in 1981. He received his B.Sc. and M.Sc. in electronics and communications engineering from Cairo University, Egypt in 2004 and 2007, respectively. He is currently working toward his Ph.D. in the Analog and Mixed-Signal Center (AMSC), Texas A&M University, College Station, TX. During spring 2008, he was an intern at Rice Nanoscale Systems Laboratory (NSL), Rice University, Houston, TX, where he was working on non-autonomous chaotic oscillators and 60 GHz receivers. He held a summer internship with the analog and mixed-signal group at QUALCOMM Inc. in San Diego, CA. His research interests include data-converters and multi-standard wireless receivers.