# S E M I N A R

## Room 104A ZEC

Thursday, February 18, 2010    3:55 - 5:10 P.M.

by

Rinaldo Castello

University of Pavia, Pavia, Italy

Abstract: Class-G Headphone Driver in 65nm CMOS Technology

A. Lollio1, G. Bollati2, R. Castello1

1University of Pavia, Pavia, Italy

2Marvell, Pavia, Italy

A 65nm CMOS Class-G headphone driver operates from +-1.4V and +-0.35V supplies. At low power level it uses the low voltage supply to reduce the dissipation to 1.63mW @ Pout=0.5mW into 32Ω. At higher power level, the smooth transition between the voltage supply rails allows a THD+N better than -80dB for Pout≤16mW into 32Ω. The SNR is 101dB, quiescent power is 0.41mW and active die area is 0.14mm2.

3.3GHz DCO with a Frequency Resolution of 150Hz for All-Digital PLL

L. Fanori, A. Liscidini, R. Castello

University of Pavia, Pavia, Italy

A 3.3GHz DCO that achieves a minimum frequency quantization step of 150Hz without any dithering is presented. The fine digital tuning is obtained through a capacitive degeneration of a portion of the transistor switching pair used in a classical LC-tank oscillator. The DCO exhibits a phase noise of -127.5dBc/Hz @ 1MHz drawing 16mA from a 1.8V supply, resulting in an FoM of 183dBc/Hz. The active area is 700um×450um.

Rinaldo Castello was born in Genova, Italy, in 1953. He graduated from the University of Genova in 1977. He received the Ph. D. from the  University of California, Berkeley, in 1984.  From 1983 to 1985 he was a Visiting Assistant Professor at the EECS  department of the University of California, Berkeley. In 1987 he joined the Department  of Electronics of the University of Pavia where he is now a Full Professor. He has been acting as a Consultant for ST-Microelectronics, Milan, Italy for almost 20 years and from 1998 to 2005 he was the Scientific Director of a joint  research centre between the University of Pavia and ST-Microelectronics, located in Pavia, Italy. Dr. Castello was a member of the technical program committee of  the European Solid State Circuit Conference (ESSCIRC) and of the International Solid State Circuit Conference (ISSCC). He was Technical Chair of ESSCIRC '91 and General Chair  of  ESSCIRC 2002. He was the Associate Editor for  Europe of the IEEE J. Solid-State Circuits from '94 to '96. From 2000 to 2008 he  has been a Distinguished Lecturer of the Solid State Circuit Society of IEEE. Prof Castello was named one of the outstanding contributors  for the first 50 years of the ISSCC. He was also a co-recipient of  the Best Student Paper Award at the 2005 Symposium on VLS. He is a Fellow of IEEE.