# S E M I N A R

## Room 223C ZEC

Thursday, March 12, 2009    3:55 - 5:10 P.M.

DRF Oscillator Based on a Passive RC Bandpass Filter

by

Sang Wook Park

Texas A&M University

College Station, TX

Abstract: A passive RC band-pass filter (BPF) based voltage-controlled-oscillator (VCO)operating at 2.5 GHz is presented. In GHz frequency range, a preferred type of an oscillator is either LC oscillator or a ring oscillator. LC oscillator exhibits an excellent phase noise performance with expensive inductors. On the other hand, a ring oscillator can be built with a cheap fabrication cost. However, it has a poor phase noise and jitter performance and is sensitive to a power supply noise. This work proposes a RC BPF-based oscillator. Its property is closer to a LC oscillator rather than a ring oscillator and, as a result, exhibits a better jitter performance against a power supply noise   To prove the  proposed concept, a RC BPF-based oscillator was designed and 2.5 GHz and a phase noise was measured as -95.4 dBc/Hz at 1 MHz offset.   Power consumption was 2.86 mW with a

1.3V supply voltage.

Sang Wook Park was born in Seoul, Korea, in 1970. He received the B.S. and M.S.
degree in Electronic Engineering from Yonsei University, Seoul, in 1993 and 1996,
respectively.  From 1996 to 2002, he was with LG Semiconductor and HYNIX S Korea, where he was involved in the characterization of CMOS RF processes.
His research interests include frequency synthesizers, high-speed and low-power
analog IC design, and RF IC design for wireless communication.