# S E M I N A R

## Room 104A ZEC

Thursday, March 4, 2010    3:55 - 5:10 P.M.

A 32mW 1.25GS/s 6b 2b/step SAR ADC in 0.13μm CMOS

by

Shouli Han

Silicon Laboratories

Austin, Texas

Abstract: A 1.25 GS/s 6b ADC is implemented in a 0.13 mum digital CMOS process by time-interleaving two SAR ADCs with 2.5 GHz internal clock frequency that converts 6 bits in 3 cycles. 5.5b ENOB at 1.25 GS/s and 5.8b ENOB at 1 GS/s are achieved without any off-line calibration, error correction or post processing. The entire ADC consumes 32 mW at 1.25 GS/s including T/H and reference buffers, and occupies 0.09 mm2.

Shouli Han (M’98) received the B.S. degree in Electronic Engineering and the M.S. degree in Computer Science and Engineering, both from Shanghai Jiao Tong University, P. R. China, in 1992 and 1995, respectively, and the Ph.D. degree in Electrical Engineering from Texas A&M University, College Station, in 2002. He is with Silicon Laboratories, Austin, and was on leave from leave from UT Austin from 2008 to 2009. He was with the Department of Electrical and Computer Engineering, the University of Texas at Austin, from 2002 to 2009. During his graduate study from 1997 to 2002 at Texas A&M, he was a graduate Research Assistant at Analog and Mixed-Signal Center (AMSC) under the advice of Prof. Sanchez-Sinencio and Teaching Assistant at the Department of Electrical Engineering. His research interests include low power and high speed A/D and D/A converters, RF circuits, and high performance analog and mixed-signal integrated circuits.