# S E M I N A R

## Room 119B ZEC

Tuesday, February 28, 2006    3:55 p.m. -  5:10 p.m.

Design of Clock and Data Recovery Loops For Giga-bits

Serial Data Links

by

Shanfeng Cheng

#### Dept. of Electrical and Computer Engineering

College Station, TX 77843-3128

Abstract:  Giga-bits serial data links are widely used in modern wireline data communication applications. These applications include optical transceivers and backplane transceivers. The optical transceivers cover the standards of SONET OC-48/STM-16 and SONET OC-192/STM-64, etc. The backplane transceivers cover the standards PCI Express, Serial ATA, HyperTransport, XAUI, etc. Only the data is transmitted over the channel in these applications. Thus clock and data recovery (CDR) loop is an indispensible and critical module on the receiver side. The CDR is used to recover the clock from the data stream and re-time the data, which is then further split into several low-speed data streams by demultiplexers for fully-digital processing. This presenation covers the fundamental topics related to the design of CDR including both system-level trade-offs and block-level optimization. It also covers the design of a 10Gb/s CDR for SONET OC-192 applications.

Shanfeng Cheng received his B.Sc. degree (1998) and MS degree (2001) from Department of Electrical Engineering, Fudan University, Shanghai, China. He is currently working towards Ph.D. degree in Analog & Mixed-signal Center, Texas A&M University. He worked at Broadcom as engineering intern on Serial ATA II transceivers from July 2005 to Dec 2005. His main research interests cover the design of PLLs and CDRs for high-speed data communication systems.