# S E M I N A R

## Room 227A ZEC

Wednesday, October 18, 2006,   3:00 p.m. -  3:50 p.m.

### A Power Efficient 2.5MS/s 14bit Sigma-Delta

### Modulator for A/D Conversion

by

Shouli Yan

Department of Electrical and Computer Engineering

The University of Texas at Austin

Abstract: There are two parts in this seminar. In the first part, we introduce the operating principles of sigma-delta A/D converters. Oversampling & noise shaping concepts and sigma-delta modulator architectures are reviewed. In the second part, we present our power efficient 14bit 2.5MS/s single-bit delta-sigma modulator. Switched-capacitor biased pseudo-differential split-path cascode amplifiers are proposed to achieve high power efficiency and small die area for a 14-bit 2.5MS/s sigma-delta modulator. Sufficient power supply rejection is maintained through the biasing circuit. A novel signal and reference sampling network eliminates input common-mode voltages and relaxes opamp linearity requirements. A prototype chip has been designed in a 0.25μm CMOS technology with a core area of 0.27mm2. Measurement results show 84dB dynamic range is achieved within the 1.25MHz bandwidth clocked at 120MHz, dissipating 14mW at 2.4V, including the two on-chip voltage reference buffers.

Shouli Yan (M’98) received the Ph.D. degree in Electrical Engineering from Texas A&M University, College Station, in 2002, and the B.S. degree in Electronic Engineering and the M.S. degree in Computer Science and Engineering, both from Shanghai Jiao Tong University, P. R. China, in 1992 and 1995, respectively. He has been an assistant professor at the Department of Electrical and Computer Engineering, the University of Texas at Austin, since 2003. During his graduate study from 1997 to 2002 at Texas A&M, he was a graduate Research Assistant at Analog and Mixed-Signal Center (AMSC) under the advice of Prof. Sanchez-Sinencio and Teaching Assistant at the Department of Electrical Engineering. In Fall 1999, he interned at Analog and Mixed-Signal Division of Texas Instruments, Inc., Dallas, working on low power low distortion audio power amplifier design. He was with Silicon Laboratories, Inc., Austin, in Summer 2003. His research interests include A/D and D/A converters, RF circuits, and high performance analog and mixed-signal integrated circuits.