# S E M I N A R

## Room 223D ZEC

Monday, October 3, 2011    3:00 - 3:50 P.M.

A Low-Power, 26-GHz Transformer-Based Regulated Cascode Transimpedance Amplifier in 0.25µm SiGe BiCMOS

by

Cheng Li

Texas A&M University

AMSC

Abstract: A 26 GHz transimpedance amplifier (TIA) with transformer-based regulated cascode (RGC) input stage is presented and analyzed. The transformer enhances the effective transconductance of the TIA’s input common-base transistor; reducing the input resistance and providing considerable bandwidth extension. The TIA is implemented in a 0.25µm BiCMOS technology. Measurement shows the single-ended transimpedance gain of 53dBΩ with -3dB bandwidth of 26 GHz. Total chip power, including an output buffer, is 28.2mW from a 2.5V supply; while core TIA power is 8.2mW. The measured average input-referred noise current spectral density is 21.3   . Total chip area, including pads, is 960µm×780µm.

Cheng Li received the B.E. degree in Electrical Engineering from Southeast University, China, and Master degree from Illinois Institute of Technology, Chicago, Illinois. He is currently pursuing the Ph.D. degree at Texas A&M University. His current research interests include high speed transceiver circuits for optical communication, and photonic interconnects for Network-on-Chip system.